## Slide 1: Computer Networks [OSI Model]

## Slide 2: OSI Model
OSI stands for Open System Interconnection is a reference model
that describes how information from a software application in one
computer moves through a physical medium to the software
application in another computer.
OSI consists of seven layers, and each layer performs a particular
network function.
OSI model was developed by the International Organization for
Standardization (ISO) in 1984, and it is now considered as an
architectural model for the inter-computer communications.
OSI model divides the whole task into seven smaller and manageable
tasks. Each layer is assigned a particular task.
Each layer is self-contained, so that task assigned to each layer can be
performed independently.

## Slide 3: Characteristics of OSI Model

## Slide 4: Characteristics of OSI Model
OSI Upper Layer
It mainly deals with the application related issues, and they are implemented only in the software.
The application layer is closest to the end user. Both the end user and the application layer interact with the software applications.
An upper layer refers to the layer just
above another layer.
OSI Lower Layer
It deals with the data transport issues.
The data link layer and the physical layer are implemented in hardware and software.
The physical layer is the lowest layer of the OSI model and is closest to the physical medium.
The physical layer is mainly responsible for placing the information on the physical medium.

## Slide 5: 7 Layers of OSI Model
There are the seven OSI layers. Each layer has different functions.
A list of seven layers are given below:
  Physical Layer
  Data-Link Layer
  Network Layer
  Transport Layer
  Session Layer
  Presentation Layer
  Application Layer

## Slide 6: 7 Layers of OSI Model

## Slide 7: Physical Layer
The main functionality of the physical layer is to transmit the individual bits from one node to another node.
It is the lowest layer of the OSI model.
It establishes, maintains and deactivates the physical connection.
It specifies the mechanical, electrical and procedural network interface specifications.

## Slide 8: Physical Layer

## Slide 9: Functions of a Physical Layer
It defines the way how two or more devices can be connected
Line
Configuration: physically.
It defines the transmission mode whether it is simplex, half- duplex or full-duplex mode between the two devices on the network.
Data Transmission:
Topology:
It defines the way how network devices are arranged.
It determines the type of the signal used for transmitting the information.
Signals:

## Slide 10: Data-Link Layer
This layer is responsible for the error-free transfer of data frames.
It defines the format of the data on the network.
It provides a reliable and efficient communication between two or more devices.
It is mainly responsible for the unique identification of each device that resides on a local network.
It contains two sub-layers:
  Logical Link Control Layer
  Media Access Control Layer

## Slide 11: Data-Link Layer
It is responsible for transferring the packets to the Network layer of the receiver that is receiving.
It identifies the address of the network layer protocol from the header.
It also provides flow control.
Logical Link Control Layer
A Media access control layer is a link between the Logical Link Control layer and the network's physical layer.
It is used for transferring the packets over the network.
Media Access Control Layer

## Slide 12: Data-Link Layer

## Slide 13: Functions of the Data-link Layer
Framing:
  The data link layer translates the physical's raw bit stream into packets known as Frames.
  The Data link layer adds the header and trailer to the frame.
  The header which is added to the frame contains the hardware destination and source address.

## Slide 14: Functions of the Data-link Layer
Physical Addressing:
  The Data link layer adds a header to the frame that contains a destination address.
  The frame is transmitted to the destination address mentioned in the header.
Flow Control:
  Flow control is the main functionality of the Data-link layer.
  It is the technique through which the constant data rate is maintained on both the sides so that no data get corrupted.
  It ensures that the transmitting station such as a server with higher processing speed does not exceed the receiving station, with lower processing speed.

## Slide 15: Functions of the Data-link Layer
Error Control:
  Error control is achieved by adding a calculated value CRC (Cyclic Redundancy Check) that is placed to the Data link layer's trailer which is added to the message frame before it is sent to the physical layer.
  If any error seems to occur, then the receiver sends the acknowledgment for the retransmission of the corrupted frames.
Access Control:
  When two or more devices are connected to the same communication channel, then the data link layer protocols are used to determine which device has control over the link at a given time.

## Slide 16: Network Layer

## Slide 17: Network Layer
It is a layer 3 that manages device addressing, tracks the location of devices on the network.
It determines the best path to move data from source to the destination based on the network conditions, the priority of service, and other factors.
The Data link layer is responsible for routing and forwarding the packets.
Routers are the layer 3 devices, they are specified in this layer and used to provide the routing services within an internetwork.
The protocols used to route the network traffic are known as Network layer protocols. Examples of protocols are IP and IPv6.

## Slide 18: Functions of Network Layer
An internetworking is the main responsibility of the network layer. It provides a logical connection between different devices.
Internetworking:
A Network layer adds the source and destination address to the header of the frame.
Addressing is used to identify the device on the internet.
Addressing:
Routing is the major component of the network layer, and it determines the best optimal path out of the multiple paths from source to the destination.
Routing:
A Network Layer receives the packets from the upper layer and converts them into packets.
This process is known as Packetizing. It is achieved by internet protocol (IP).
Packetizing:

## Slide 19: Transport Layer

## Slide 20: Transport Layer
The Transport layer is a Layer 4 ensures that messages are transmitted in the order in which they are sent and there is no duplication of data.
The main responsibility of the transport layer is to transfer the data completely.
It receives the data from the upper layer and converts them into smaller units known as segments.
This layer can be termed as an end-to-end layer as it provides a point-to-point connection between source and destination to deliver the data reliably.

## Slide 21: Protocols Used in Transport Layer
Transmission Control
Protocol
User Datagram
Protocol
It is a standard protocol that allows the systems to communicate over the internet.
It establishes and maintains a connection between hosts.
When data is sent over the TCP connection, then the TCP protocol divides the data into smaller units known as segments. Each segment travels over the internet using multiple routes, and they arrive in different orders at the destination.
The transmission control protocol reorders the packets in the correct order at the receiving end.
User Datagram Protocol is a transport layer protocol.
It is an unreliable transport protocol as in this case receiver does not send any acknowledgment when the packet is received, the sender does not wait for any acknowledgment. Therefore, this makes a protocol unreliable.

## Slide 22: Functions of Transport Layer
Service-point addressing:
Computers run several programs simultaneously due to this reason, the transmission of data from source to the destination not only from one computer to another computer but also from one process to another process.
The transport layer adds the header that contains the address known as a service-point address or port address.
The responsibility of the network layer is to transmit the data from one computer to another computer and
the responsibility of the transport layer is to transmit the message to the correct process.
Segmentation and reassembly:
When the transport layer receives the message from the upper layer, it divides the message into multiple segments, and each segment is assigned with a sequence number that uniquely identifies each segment.
When the message has arrived at the destination, then the transport layer reassembles the message based on their sequence numbers.

## Slide 23: Functions of Transport Layer
Connection control:
Transport layer provides two services Connection-oriented service and connectionless service.
A connectionless service treats each segment as an individual packet, and they all travel in different routes to reach the destination.
A connection-oriented service makes a connection with the transport layer at the destination machine before delivering the packets. In connection-oriented service, all the packets travel in the single route.
Flow control:
The transport layer also responsible for flow control but it is performed end-to-end rather than across a single link.
Error control:
The transport layer is also responsible for Error control. Error control is performed end-to-end rather than across the single link.
The sender transport layer ensures that message reach at the destination without any error.

## Slide 24: Session Layer
The Session layer is used to establish, maintain and synchronizes the interaction between communicating devices.

## Slide 25: Functions of Session Layer
Dialog control:
Session layer acts as a dialog controller that creates a dialog between two processes, or we can say that it allows the communication between two processes which can be either half-duplex or full-duplex.
Synchronization:
Session layer adds some checkpoints when transmitting the data in a sequence. If some error occurs in the middle of the transmission of data, then the transmission will take place again from the checkpoint.
This process is known as Synchronization and recovery.

## Slide 26: Presentation Layer
A Presentation layer is mainly concerned with the syntax and semantics of the information exchanged between the two systems.
It acts as a data translator for a network.
This layer is a part of the operating system that converts the data from one presentation format to another format.
The Presentation layer is also known as the syntax layer.

## Slide 27: Presentation Layer

## Slide 28: Functions of Presentation Layer
Translation:
The processes in two systems exchange the information in the form of character strings, numbers and so on. Different computers use different encoding methods, the presentation layer handles the interoperability between the different encoding methods.
It converts the data from sender-dependent format into a common format and changes the common format into receiver-dependent format at the receiving end.
Encryption:
Encryption is needed to maintain privacy. Encryption is a process of converting the sender- transmitted information into another form and sends the resulting message over the network.
Compression:
Data compression is a process of compressing the data, i.e., it reduces the number of bits to be transmitted. Data compression is very important in multimedia such as text, audio, video.

## Slide 29: Application Layer
An application layer serves as a window for users and application processes to access network service.
It handles issues such as network transparency, resource allocation, etc.
An application layer is not an application, but it performs the application layer functions.
This layer provides the network services to the end-users.

## Slide 30: Application Layer

## Slide 31: Functions of Application Layer
An application layer allows a user to access the files in a remote computer, to retrieve the files from a computer and to manage the files in a remote computer.
File transfer, access, and management (FTAM):
An application layer provides the facility for email forwarding and storage.
Mail services:
An application provides the distributed database sources and is used to provide that global information about various objects.
Directory services: