## Slide 1: Computer Networks [TCP/IP Model]

## Slide 2: TCP/IP Model
The TCP/IP model was developed prior to the OSI model.
The TCP/IP model is not exactly similar to the OSI model.
The TCP/IP model consists of five layers:
  Application Layer
  Transport Layer
  Network Layer
  Data Link Layer
  Physical Layer

## Slide 3: TCP/IP Model
The first four layers provide physical standards, network interface, internetworking, and transport functions that correspond to the first four layers of the OSI model and these four layers are represented in TCP/IP model by a single layer called the application layer.
TCP/IP is a hierarchical protocol made up of interactive modules, and each of them provides specific functionality.
Here, hierarchical means that each upper-layer protocol is supported by two or more lower-level protocols.

## Slide 4: Functions of TCP/IP Layers

## Slide 5: Network Access Layer
A network layer is the lowest layer of the TCP/IP model.
A network layer is the combination of the Physical layer and Data Link
layer defined in the OSI reference model.
It defines how the data should be sent physically through the network.
This layer is mainly responsible for the transmission of the data
between two devices on the same network.
The functions carried out by this layer are encapsulating the IP datagram into frames transmitted by the network and mapping of IP addresses into physical addresses.
The protocols used by this layer are ethernet, token ring, FDDI, X.25, frame relay.

## Slide 6: Internet Layer
An internet layer is the second layer of the TCP/IP model.
An internet layer is also known as the network layer.
The main responsibility of the internet layer is to send the packets from any network, and they arrive at the destination irrespective of the route they take.
Protocols used in this layers are:
  IP Protocol
  ARP Protocol
  ICMP Protocol

## Slide 7: IP Protocol
IP protocol is the most significant part of the entire TCP/IP suite.

## Slide 8: Host to Host Communication
Responsibilities of IP Protocol
IP Addressing
Data Encapsulation and Formatting
Fragmentation and Reassembly
Routing

## Slide 9: IP Addressing
IP Addressing
Host to Host Communication
Data Encapsulation and Formatting
Fragmentation and Reassembly
Routing
This protocol implements logical host addresses known as IP addresses.
The IP addresses are used by the internet and higher layers to identify the device and to provide internetwork routing.
IP Addressing

## Slide 10: IP Addressing
IP Addressing
Host to Host Communication
Data Encapsulation and Formatting
Fragmentation and Reassembly
Routing
It determines the path through
which the data is to be
transmitted.
Host to Host
Communication

## Slide 11: IP Addressing
IP Addressing
Host to Host Communication
Data Encapsulation and Formatting
Fragmentation and Reassembly
Routing
An IP protocol accepts the data from the transport layer protocol.
An IP protocol ensures that the
data is sent and received
securely, it encapsulates the data
into message known as IP
datagram.
Data Encapsulation and Formatting

## Slide 12: IP Addressing
IP Addressing
Host to Host Communication
Data Encapsulation and Formatting
Fragmentation and Reassembly
Routing
The limit imposed on the size of the IP datagram by data link layer protocol is known as Maximum Transmission unit (MTU).
If the size of IP datagram is greater than the MTU unit, then the IP protocol
splits the datagram into smaller units so that they can travel over the local network.
Fragmentation can be done by the sender or intermediate router.
At the receiver side, all the fragments are reassembled to form an original message.
Fragmentation and Reassembly

## Slide 13: IP Addressing
IP Addressing
Host to Host Communication
Data Encapsulation and Formatting
Fragmentation and Reassembly
Routing
When IP datagram is sent over the same local network such as LAN, MAN, WAN, it is known as direct delivery.
When source and destination are on the distant network, then the IP datagram is sent indirectly.
This can be accomplished by routing the IP datagram through various devices such as routers.
Routing

## Slide 14: ARP Protocol
ARP stands for Address Resolution Protocol.
ARP is a network layer protocol which is used to find the physical address from the IP address.
The two terms are mainly associated with the ARP Protocol:
  ARP Request: When a sender wants to know the physical address of the device, it broadcasts the ARP request to the network.
  ARP Reply: Every device attached to the network will accept the ARP request and process the request, but only recipient recognize the IP address and sends back its physical address in the form of ARP reply. The recipient adds the physical address both to its cache memory and to the datagram header.

## Slide 15: ICMP Protocol
ICMP stands for Internet Control Message Protocol.
It is a mechanism used by the hosts or routers to send notifications regarding datagram problems back to the sender.
A datagram travels from router-to-router until it reaches its destination. If a router is unable to route the data because of some unusual conditions such as disabled links, a device is on fire or network congestion, then the ICMP protocol is used to inform the sender that the datagram is undeliverable.
An ICMP protocol mainly uses two terms:
  ICMP Test: ICMP Test is used to test whether the destination is reachable or not.
  ICMP Reply: ICMP Reply is used to check whether the destination device is
responding or not.

## Slide 16: ICMP Protocol
The core responsibility of the ICMP protocol is to report the problems, not correct them. The responsibility of the correction lies with the sender.
ICMP can send the messages only to the source, but not to the intermediate routers because the IP datagram carries the addresses of the source and destination but not of the router that it is passed to.

## Slide 17: Transport Layer
The transport layer is responsible for the reliability, flow control, and correction of data which is being sent over the network.
The two protocols used in the transport layer are
  User Datagram protocol and
  Transmission control protocol.

## Slide 18: User Datagram Protocol (UDP)
It provides connectionless service and end-to-end delivery of transmission.
It is an unreliable protocol as it discovers the errors but not specify the error.
User Datagram Protocol discovers the error, and ICMP protocol reports the error to the sender that user datagram has been damaged.

## Slide 19: Fields of User Datagram Protocol (UDP)
Source port address:
The source port address is the address of the application program that has created the message.
Destination port address:
The
destination port address is the address of the application program that receives the message.
Total length:
It defines the total number of bytes of the user datagram in bytes.
Checksum:
The
checksum is a 16-bit field used in error detection.

## Slide 20: Fields of User Datagram Protocol (UDP)
UDP does not specify which packet is lost.
UDP contains only checksum; it does not contain any ID of a data segment.

## Slide 21: Transmission Control Protocol (TCP)
It provides a full transport layer services to applications.
It creates a virtual circuit between the sender and receiver, and it is
active for the duration of the transmission.
TCP is a reliable protocol as it detects the error and retransmits the
damaged frames. Therefore, it ensures all the segments must be
received and acknowledged before the transmission is considered to
be completed and a virtual circuit is discarded.
At the sending end, TCP divides the whole message into smaller units
known as segment, and each segment contains a sequence number
which is required for reordering the frames to form an original message.
At the receiving end, TCP collects all the segments and reorders them
based on sequence numbers.

## Slide 22: Application Layer
issues of
An application layer is the topmost layer in the TCP/IP model.
It is responsible for handling high-level protocols, representation.
This layer allows the user to interact with the application.
When one application layer protocol wants to communicate with another application layer, it forwards its data to the transport layer.
There is an ambiguity occurs in the application layer. Every application cannot be placed inside the application layer except those who interact with the communication system.
  For example: text editor cannot be considered in application layer while web browser using HTTP protocol to interact with the network where HTTP protocol is an application layer protocol.

## Slide 23: Protocols of Application Layer
HTTP:
HTTP stands for Hypertext Transfer Protocol. This protocol allows us to access the data over the world wide web. It transfers the data in the form of plain text, audio, video.
It is known as a Hypertext transfer protocol as it has the efficiency to use in a hypertext environment where there are rapid jumps from one document to another.
SNMP:
SNMP stands for Simple Network Management Protocol.
It is a framework used for managing the devices on the internet by using the TCP/IP protocol suite.
SMTP:
SMTP stands for Simple Mail Transfer Protocol.
The TCP/IP protocol that supports the e-mail is known as a Simple mail transfer protocol.
This protocol is used to send the data to another e-mail address.

## Slide 24: Protocols of Application Layer
DNS:
DNS stands for Domain Name System.
An IP address is used to identify the connection of a host to the internet uniquely. But, people prefer to use the names instead of addresses.
Therefore, the system that maps the name to the address is known as Domain Name System.
TELNET:
It is an abbreviation for Terminal Network.
It establishes the connection between the local computer and remote computer in such a way that the local terminal appears to be a terminal at the remote system.
FTP:
FTP stands for File Transfer Protocol.
FTP is a standard internet protocol used for transmitting the files from one computer to another computer.